## Slide 1: The Hardware of Software Defined Radios
From Softrock to IC-7300
Bryan, G8DKK

## Slide 2: Topics
Acronyms
  Baseband definition
The DC Receiver
Some other Definitions
Software Defined Receivers (SDRs)
  Types of SDR
Tx/Rx SDRs – Future ideas
Some useful URLs

## Slide 3: Acronyms & Buzz Words
Acronyms – abbreviations
  ADC or A/D: Analogue to Digital Converter
  DAC or D/A: Digital to Analogue Converter
  DSP: Digital Signal Processor
  FPGA: Field Programmable Gate Array
  CODEC: Code/Decode
  QSD: Quadrature Sampling Detector
  I/Q: In-Phase / Quadrature Phase
  DC Rx: Direct Conversion receiver
  Baseband: next slide

## Slide 4: Baseband – what is it?
A section of continuous electromagnetic spectrum starting at approx. 0Hz and extending to a frequency defined by the user
The Baseband bandwidth is therefore determined by the maximum frequency
0 1kHz 10kHz 100kHz 1MHz 10MHz 100MHz 1GHz

## Slide 5: The Direct Conversion Receiver
Bandpass Filter
Mixer
Low Pass Filter
Local Osc
VFO
Low Noise Amplifier
Output Amplifier

## Slide 6: Bandwidth
The difference in frequency between the highest and lowest points in a device or circuit
A superhet Rx would have -3dB IF Bandwidths of:
  A few tens of Hz (500Hz) for CW
  A little less than 3kHz for SSB
  12kHz to 13kHz for FM
A SDR has additional limits such as:
  ADC sampling rate and/or baseband bandwidth

## Slide 7: Analogue to Digital Converter
As the name suggests this device has an analogue input amplifier and a digital output.
  The digital output can be in either parallel or series formats
A sampling clock is needed to generate the output.
  The clock runs at least twice the maximum frequency of the input

## Slide 8: Software Defined Radios
The 3 most common types:
  Direct Conversion SDR
  Superheterodyne (superhet) SDR
  Direct Sampling SDR
The superhet with SDR is a hybrid of analogue and digital technology
Some SDRs use both DC & Direct Sampling

## Slide 9: Softrock Lite II SDR

## Slide 10: Softrock Block Diagram
Bandpass Filter
Signal Splitter
Low Noise Amplifier
Low Noise Amplifier
I
Q
÷2
÷2
Crystal Oscillator
Quadrature Sampling Detector
To PC

## Slide 11: Softrock Board - Underside

## Slide 12: Softrock, Processing Output
Processing of the I/Q signals takes place in the CODEC in the PC sound card controlled by a software program. Bandwidths of 48kHz or 96kHz are usual
  This includes selection of mode, demodulation of the signal and conversion to an audio output to the PC speakers and/or headphone output
More complex SDRs will digitise the I/Q outputs via an on-board CODEC and convert to a digital bit stream to be sent over a USB connection

## Slide 13: DC SDR - RFSpace SDRIQ
100kHz – 30MHz Rx, 192kHz max SDR bandwidth over USB

## Slide 14: SDR-IQ Internal

## Slide 15: DC SDR – SDRPlay RSP-1
10kHz – 2GHz Rx, 8MHz SDR bandwidth over USB

## Slide 16: SDR Play RSP-1 Internal

## Slide 17: Elecraft KX3 – DC SDR

## Slide 18: Superhet SDRs
These are probably the most common at the moment as most of the manufacturers removed the analogue demodulator and early audio stages from existing transceivers.
Replaced by a final low frequency IF conversion followed by a SDR demodulator and modulator

## Slide 19: Superhet SDRs
Bandpass Filter
Mixer
IF Amplifier
Mixer
Local Osc VFO
SDR IF & Audio
Fixed LO
Conventional front end, SDR final IF with demod to AF output

## Slide 20: Elecraft K3/K3s SDR Final IF

## Slide 21: Kenwood TS590SG SDR Final IF

## Slide 22: Icom IC-9100 SDR Final IF

## Slide 23: Yaesu FT-991A SDR Final IF

## Slide 24: Direct Sampling SDRs
Bandpass Filter
ADC
FPGA
ADC Clock
USB?
μP

## Slide 25: Perseus SDR Rx
10kHz - 30MHz, 80Msamples/sec ADC, 1.6MHz Baseband B/W

## Slide 26: Perseus – Internal

## Slide 27: Elad FDM Duo

## Slide 28: Icom IC-7300

## Slide 29: Tx/Rx SDRs – The Future
Although most of the manufacturers are now integrating SDR into their products where does this leave the amateur community with regard to experimentation?
There are some building blocks available at reasonable prices

## Slide 30: Analog Devices Pluto SDR Tx/Rx
325MHz – 3800MHz Rx/Tx, at up to 61.44Msps

## Slide 31: Lime SDR Transceiver

## Slide 32: Last Slide
That’s all folks
Questions

## Slide 33: Useful URLs
www.wb5rvz.com/sdr
www.fivedash.com (KB9YIG)
www.rfspace.com
www.sdrplay.com
www.sdr-kits.net
www.kanga-products.co.uk